## Slide 1: A Locomotion Interface with the Exact Haptics and Kinesthesia
Daiki Sato, Masataka Ezoe,
Arisa Shimizu, Ayaka Hino,
Katsuya Kikuchi, Yurio Hosaka,
Hironori Mitake, Shoichi Hasegawa
Tokyo Institute of Technology
Notes: Today, we will talk about our emerging technology project, VibroSkate

## Slide 2: Introduction
Notes: VibroSkate is a small and low-cost skateboard simulator which provides a virtual moving ground.
When the player rides on the device and kicks the treadmill, the virtual skateboard will go ahead just like a real one. And you can change the direction by moving your center of gravity. The more you kick the treadmill the faster the skateboard will go. While playing, you will feel the vibration through your feet as if you are skateboarding on real ground.

## Slide 3: Background
VR Technology for Family Use
  HMD
  High Resolution CG
  Large VR World Data
What about House Sized Locomotion Devices?
“Omni” Virtuix
“Oculus Rift” Oculus VR, Inc.
“Japanese Otaku City” ZENRIN
“Virtualizer” CYBERITH
Notes: Now, I'd like to start with background. As growth of virtual reality technologies such as head mounted display or computer graphics, it became more and more easy to experience huge virtual world in our own house. However, major way to move around those virtual worlds are keyboard, mouse or gamepad. These kind of input methods are very different from real moving methods such as walking or riding a bicycle, causing poor experience in virtual worlds. Therefore, we need a locomotion interface that is small enough to fit in a house, and can represent good moving sensation.

## Slide 4: Locomotive Perception Mechanism
Vection
  Movement of Peripheral Vision
Vestibular Sensation
  Linear / Angular Acceleration
Somatic Sensation
  Kinesthesia (from Joints, Muscles, Tendons)
  Tactile Sensation
Notes: before talking about locomotion interfaces, I’d like to introduce how people percept locomotion.
First is vection. When peripheral vision moves, a viewer feels like he has moved.
Second is vestibular sensation. The sensors are placed in inner ears, and can sense linear and angular acceleration.
The last is somatic sensation. You can feel your movement by joints, muscled, tendons and tactile sensation.

## Slide 5: Conventional Locomotion Interfaces
size
Vestibular Sensation
Somatic Sensation
“Cyberith virtualizer: a locomotion device for virtual reality” T.Cakmak and H.Hager SIGGRAPH 2014
“Control design and experimental evaluation of the 2D CyberWalk platform” De Luca, A. et al., IROS 2009
“Inertial Force Feedback for a Locomotion Interface” R.R.Christensen et al. , Presence, 2000
Notes: Now, I’ll talk about locomotion interfaces.
conventional house size locomotion interfaces do not reproduce exact vestibular sensation and somatic sensation, because they want to make the device small, light and low-cost.

## Slide 6: Conventional Locomotion Interfaces
size
Vestibular Sensation
Somatic Sensation
“Cyberith virtualizer: a locomotion device for virtual reality” T.Cakmak and H.Hager SIGGRAPH 2014
“Control design and experimental evaluation of the 2D CyberWalk platform” De Luca, A. et al., IROS 2009
“Inertial Force Feedback for a Locomotion Interface” R.R.Christensen et al. , Presence, 2000
Notes: On the other-hand, locomotion interfaces in labs are too big for home use, so that they allow users to actually walk around to reproduce vestibular sensation.
Can’t we incorporate good points of these interfaces? That is, a locomotion interface system that is small and can give well moving sensation.

## Slide 7: Conventional Locomotion Interfaces
size
Vestibular Sensation
Somatic Sensation
“Cyberith virtualizer: a locomotion device for virtual reality” T.Cakmak and H.Hager SIGGRAPH 2014
“Control design and experimental evaluation of the 2D CyberWalk platform” De Luca, A. et al., IROS 2009
“Inertial Force Feedback for a Locomotion Interface” R.R.Christensen et al. , Presence, 2000
Notes: Christensens’ research gave us a hint. They show that kinesthesia and feedback force gives a strong moving sensation, even without giving vestibular sensation.

## Slide 8: Conventional Locomotion Interfaces
size
Vestibular Sensation
Somatic Sensation
“Cyberith virtualizer: a locomotion device for virtual reality” T.Cakmak and H.Hager SIGGRAPH 2014
“Control design and experimental evaluation of the 2D CyberWalk platform” De Luca, A. et al., IROS 2009
“Inertial Force Feedback for a Locomotion Interface” R.R.Christensen et al. , Presence, 2000
VibroSkate
Notes: And so, our design follows this path. By omitting the feedbacks for vestibular sensation but reproducing exact kinesthesia and vibration to the user’s feet, we achieved to make the device small enough for home use, and can give good moving sensation.

## Slide 9: How VibroSkate Reproduce Kinesthesia
Real skateboard
VibroSkate
Notes: VibroSkate brings together the exact haptics and kinesthesia of feet.
On real skateboard, when you kick the ground to go further, you can feel the kinesthesia and the feedback force on your feet’s joints and muscles.

## Slide 10: How VibroSkate Reproduce Kinesthesia
How VibroSkate Reproduce Kinesthesia
Real skateboard
VibroSkate
Notes: On VibroSkate, the device detects the kicking force and simulates the dynamics between the skateboard and the player. And then the speed of the treadmill is controlled by the velocity of the simulated skateboard. This achieves the exact feet kinesthesia and feedback force.

## Slide 11: How VibroSkate Reproduce Kinesthesia
Real skateboard
VibroSkate
Notes: In fact, player is not moving actually, so the kicking force must be balanced with the force on the foot, standing on the skateboard and the force on the hand, grabbing a handrail.
This is different from the real skateboarding, however, the player’s focus is on kicking foot, so this doesn’t matter for the reality of skateboarding.

## Slide 12: Implementation
Gyroscope & Accelerometer
Change direction by tilting
Geared motor for driving belt
Force sensor
http://www.aandd.co.jp
Notes: This is the overview of VibroSkate.
The device is consist of skateboard, treadmill, head mounted display and handrail.
the force sensor for detecting kicking force is mounted inside the treadmill. The motor for driving the belt is mounted on top of the treadmill. Next to the treadmill, there is a skateboard with gyroscope and accelerometer mounted on back side to detect the tilt of the skateboard.
next, our co-author Arisa Shimizu will talk about vibration display part of this device.

## Slide 13: Introduction - Vibration
Haptics on feet
Kinesthesia
Vibration
Vibration in skateboarding
Textures of ground
Sensation of moving
Notes: Next, I will talk about vibration display part in VibroSkate.
In real skateboarding, not only kinesthesia but also vibration is important.
Vibration on our feet tells us material of the ground, texture of ground surface, and moving velocity.
VibroSkate reproduces vibration of real skatebording, so that we can feel as if we're running through real ground.

## Slide 14: Textures & Materials
Reproducing texture by vibration on the feet soles
  "A multi-modal floor-space for experiencing material deformation underfoot in virtual reality“ (Law, A.W. et al., 2008)
Reproducing material by vibration
  "Reality-based models for vibration feedback in virtual environments“ (Okamura et al., 2001)
In skateboarding, textures : textures from ground!
Notes: There are prior researches on reproducing materials and textures with vibration.
Okamura's research in 2001 showed dumping sinusoidal vibration on finger is effective to reproduce sensation of material while tapping.
More recent research by Law et al., reproduced fantastic feeling of walking on snow and ice, by vibrating floor according to foot pressure.
As for skatebording, wheels rolling over various ground surface causes different vibrations. It tells us road condition, and also makes us fun.

## Slide 15: Related works – Sensation of moving by vibration
Strengthen sensation of moving by vibration on the feet soles
  "Vibrotactile inputs to the feet can modulate vection“ (Farkhatdinov et al. , 2013)
Combining with treadmill
Stronger sensation of moving
Notes: On the other hand, There is a research revealing that vibration on feet can strengthen sensation of motion : in fact, vibration on feet can modulate vection.
It shows that strong sensation of moving in VibroSkate is not only from realistic kinesthesia as we talked before, but also from exact vibration according to running speed.

## Slide 16: Vibration display in VibroSkate
20W audio amplifier
with bass boost
Transducer for BodySonic
Notes: Next, I will talk about implementation.
2 large transducers are inside the skateboard unit of VibroSkate.
We used the transducers originally made for BodySonic: that is, vibrating body according to music so that we can feel heavy bass sound.
Transducers are driven with 20W audio amplifier with bass boost.

## Slide 17: Sampling vibration
Sampled using a real skateboard rolling over different surfaces
2 accelerometers
  Near base of the wheel
3 different speeds
  0.7, 1.0, 2.0[m/s]
accelerometer
Notes: Vibrations are sampled using a real skateboard rolling over different surfaces using 2 accelerometers.
We dragged the skateboard in constant speed carefully.
Sampling was done in 3 different speeds for each types of ground : 0.7m/s, 1m/s, 2m/s.

## Slide 18: Vibration of different materials
Sampled 15 different textures of ground
  Different material
  Different texture
Brick
Tile
Wood deck
Asphalt
Notes: We sampled 15 different grounds.
Here I show you some examples of recorded vibration.<<再生>>
These vibrations reflect ground materials like wood or metal, and surface textures like roughness.
Vibrations from tiles and bricks were cyclic, reflecting its periodic pattern of surface.

## Slide 19: Interpolation of different speed of vibration
Chart: 
| 0 | 0.35
 | -2400 | 466
 | -367 | 594
 | -427 | 1200
Interpolating 3 different speeds
In slow speed, feeling like stronger vibration
  Weaken vibration
Using CRI ADX2 LE
  http://www.adx2le.com/
Normalized board speed
Pitch
Chart: 
| 0 | 0.06 | 0.11 | 0.15 | 0.29499999999999998 | 0.35 | 1
 | 0 | 0.38 | 0.87 | 1.36 | 1.64 | 0 | 0
 | 0 | 0 | 2 | 2 | 0 | 0
 | 0 | 0 | 2 | 2
Volume
Normalized board speed
Notes: While VibroSkate is running, the system playback recorded vibration with modified pitch, according to the forward / backward velocity of virtual skateboard.
Vibrations recorded with 3 different speeds, are used for each range of virtual skateboard's velocity.
The system also modifies the volume according to the speed.
Especially, recorded acceleration in slow speed creates too strong vibration, so we weakened the volume when the vitual skateboard is in low speed.
We edited these vibrations using CRI ADX2 LE.

## Slide 20: Exposition
International collegiate Virtual Reality Contest 2014
  For 4 days, over 500 people
Discovery Lab ISHIKAWA 2014
  For 2 days, about 300 people
Elderly & children also played
  Turned off crawler, only vibration
  Also enjoyed
Notes: Next, I will talk about exposition.
International collegiate Virtual Reality Contest 2014 in Japan was for 4 days and over 500 people played there.
Discovery Lab ISHIKAWA 2014 in Japan was for 2 days and about 300 people played.
There elderly & children also played VibroSkate and we turned off crawler for safety, but they enjoyed only vibration and picture on screen.

## Slide 21: Exposition – Feedback from players
Impression
  People never played skateboard also enjoyed
  To input kicking force for themselves is fun.
  Vibration and picture on screen reproduced exhilarating feeling.
  Effective to decrease motion sickness?
Problem
  For a person with experience of skateboarding noticed that VibroSkate is different from a real one.
  To feel exhilarating, we set the board speed faster
    Some people noticed the difference between board speed and vibration speed.
Notes: Next, I will show you some impressions and problems.
People never played skateboard also enjoyed VibroSkate.
To input kicking force for themselves is fun.
Vibration and picture on screen reproduced exhilarating feeling.
Maybe VibroSkate is effective to decrease motion sickness.
Problem was :
For a person with experience of skateboarding noticed that control of VibroSkate is different from a real one.
To give more exhilarating feeling, we set the board speed faster.
But some people noticed the difference between board speed and vibration speed.

## Slide 22: Future
First Haptic-based Locomotion Interface for Home
Application
  Virtual Sightseeing
  Game controller
  Exercise
  etc.
Japanese Otaku City
ZENRIN
Notes: VibroSkate is a first home-capable locomotion interface which reproduces exact haptics on feet.
It provides fan of skateboarding in VR.
As applications, it will also be useful for virtual sightseeing, gaming devices, and even for exercise.
Thank you for listening.